## Slide 1: Learning to cooperate or “How I became a good neighbor”
Milos Rovcanin

## Slide 2: Status quo
Enormous increase in a density of co-located, multi-purpose networks.

## Slide 3: Zooming in
Pretty soon, a typical household unit will be equipped with a number of
wireless networks, for all sorts of purposes: controlling temperature,
access to premises, temperature, ventilation etc.

## Slide 4: Network diversity
A huge variety of network preferences and their hardware/software capabilities:
              Wifi standards IEEE 802.11a, 802.11b, 802.11g and 802.11n (at 2.4 GHz)
              Zigbee standard IEEE 802.15.4 (at 2.4 GHz)
              6LoWPAN (RFC 4944) standard IEEE 802.15.4 (at 2.4 GHz)
              ONE-NET is an open-source standard for designed for low-cost, low-power control networks
              Bluetooth standard 802.15.1 (2.4 up to 2.8 GHz)
              Bluetooth Low Energy (Wibree) is a subset to Bluetooth V4.0 with an entirely new protocol stack for rapid build-up of simple links.
              ANT: ANT is a proprietary wireless sensor network technology operating at 2.4 GHz that provides a low-cost and ultra-low power solution for short-range wireless communication in point-to-point and more complex network topologies
Source: Texas Instruments Wireless Connectivity

## Slide 5: Sharing a common radio frequency
Communication interference is commonplace:
Interference avoidance as a basic form of inter-network cooperation

## Slide 6: A preliminary conclusion
Static grouping of mobile devices is complex, inefficient and might lead to a waste of resources
Network solutions that dynamically support at run-time cooperation between devices from different types of networks are becoming a necessity.

## Slide 7: Networks cooperating

## Slide 8: Incentive driven networking
A cross-layer, cross-network negotiation methodology for optimizing network resources

## Slide 9: Incentive driven networking
Incentive describes a high-level network behavior or a reason for cooperation:
  Describe behavioral aspects of the network
  Express the need for additional functionality
  Give an indication of the expected performance network metric
  Examples:
  High throughput, high reliability, low delay (better QoS)
  High network lifetime
  High coverage
  Low exposure
  Public access

## Slide 10: Network services
Whereas incentives indicate network goals, network services are means to realize these goals
Network services should be understood as optimization techniques that have influence over one or more incentives
Examples:
packet aggregation and sharing, MAC protocols, interference avoidance techniques …

## Slide 11
Activating network services has (positive or negative) influence not only in a network where the service is activated.
By carefully choosing which service to activate, networks can improve not only their own, but the neighboring network’s performance as well.

## Slide 12: Incentive driven networking
Step 1:
  Devices dynamically search for co-located devices with similar network preferences and hardware and/or software capabilities

## Slide 13: Incentive driven networking
Step 2:
  If such devices are found, communities consisting of interconnected objects with similar network expectations are formed on an ad hoc basis

## Slide 14: Incentive driven networking
Step 3:
  Different communities will now able to cooperate with each other by activating and sharing (software or hardware) network resources.

## Slide 15: The major issue
How to efficiently determine the optimal configuration parameters for all the participating networks, considering their high level goals and ensuring that the cooperation in mutually beneficial?

## Slide 16: A self learning approach
There is a need for a reasoning entity that will initiate and control the cooperation process.
It will use certain performance metric to make an assessment of every relevant and utilized service combination, over an entire symbiotic network.
It must be able to automatically reconfigure all the participating networks, depending on a decision it makes.

## Slide 17: A self learning approach – use case
B
A
A
Temperature sensor node (community A)
Intrusion detection sensor node (community B)
A
A
A
A
A
A
A
A
B
B
B
B
B
B
B
B
B
Sink A
Sink B
Final goal: three-tiered approach
  Phase 1: Optimization of service settings (in-layer)
  Phase 2: Selection of optimal service sets (cross-layer)
  Phase 3: Cross-network negotiation (cross-network)
    Also take into account the requirements of co-located networks
The goal:
Determine the best combinations of network services

## Slide 18: The initial approach
Linear programming (LP)
Negotiation entity (NE) collects network’s service profiles and “calculates” the optimal service set for every sub-net using an IBM’s linear programming engine

## Slide 19: Disadvantages
Requires a priori knowledge - fixed benefits and costs for activating each service:
Eli de Poorter, Pieter Becue, Milos Rovcanin, ingrid Moerman, Piet Demeester, “A negotiation-based networking methodology to enable cooperation across heterogeneous co-located networks”

## Slide 20: Disadvantages
Information about the service influences is extremely difficult to obtain:
  Simulation
  From a literature
  Assumed …
Most of this data relates to static networking cases and change drastically when some of the network parameters change.
Conclusion:
ILP solver is a poor solution for dynamic environments

## Slide 21: Possible alternatives
More adaptable to environments with fast changing parameters and much less demanding when it comes to a priory input information
  Simulators
  Mathematical modeling
  Game theory
  Machine – reinforcement learning

## Slide 22: Cognition cycle
4-steps:
  Gathering Information (GI)
  Planning Actions (PA)
  Act (A)
  Collecting Feedback

## Slide 23: Reinforcement learning
Modeled as a Markov decision process (MDP)
A decision maker goes through states: S = {S1, S2, … , S3}
Taking one of the available actions A = {a1, a2,… aN} at each step
The Bellman equation describes the learning process:
At each step, take the action that will maximize Q-value for the given state/action pair

## Slide 24: Reinforcement learning
Bellman equation:
Immediate reward
expected future reward
state transition probability

## Slide 25: The major issue
An MDP model differs from case to case. In most of them, it is not known a priory
A universal method for solving these kind of optimization problems has to be model-free

## Slide 26: Least Squares Policy Iteration - LSPI
First Introduced in:
M. Lagoudakis and R. Parr. “Model-free least-squares policy iteration”. In Proc. of NIPS, 2001.
Instead of relying on a pre-learned MDP model, an agent collect process samples
One set can be used for different policies
Additional samples can be added, during the learning process, to an existing set

## Slide 27: Least Squares Policy Iteration - LSPI
Approximates Q-function with its linear represent:
- basis functions represent a network’s feature (e.g., residual energy of s’, link quality between s and s’ etc.)
- a corresponding weight factor

## Slide 28: Least Squares Policy Iteration - LSPI
After combining the Bellman equation and it’s linear approximation:
And the corresponding matrices are given as:

## Slide 29: Least Squares Policy Iteration - LSPI
Approximated values for matrices:
- In fact represents a probability P((s’,a’) | (s,a))
To improve consistency between the approximated and the actual values:

## Slide 30: Least Squares Policy Iteration - LSPI
LSPI - strong points:
It converges faster than all other known algorithms, since the samples are used more efficiently.
It does not require fine tuning of the initial parameters such as learning rate
LSPI learns the weights of the linear functions and updates Q-values based on the most updated information regarding the features, while in other approaches agents make decisions directly based on Q-values, which may be outdated, depending on the network dynamics.
The same set of samples is used to evaluate different policies

## Slide 31: Implementation
Milos Rovcanin, Eli De Poorter, Ingrid Moerman, Piet Demeester, “A reinforcement learning based solution for cognitive network cooperation between co-located, heterogeneous wireless sensor networks”, AD HOC Networks, 17: 98-113 (2014)
Sub-net A: temperature monitoring sensor nodes
  Incentives: high network lifetime
  Available services: packet sharing, aggregation
Sub-net B: temperature sensor nodes
  Incentives: low delay, high network lifetime
  Available services: packet sharing, aggregation
B
A
A
Temperature sensor node (community A)
Intrusion detection sensor node (community B)
A
A
A
A
A
A
A
A
B
B
B
B
B
B
B
B
B
Sink A
Sink B

## Slide 32: Implementation
A service combination represent a state
S = {s0,s1,s2,s3}
Activating or deactivating a service
is considered to be an action
A = {a1,a2,a3,a4}
Reuse of the existing data (CPLEX ILP Solver)
- reduced set of states and constrained actions

## Slide 33: Implementation
Two phase process:
  Exploration phase – Exhaustive search through the state problem space, investigating every service combination
  Exploitation phase – use “Epsilon greedy” algorithm to enforce optimal decisions, while staying versatile to adapt to possible network condition changes

## Slide 34: Implementation
Exploration phase:
  Collect the information about
  every state/action pair, using the
  memoryless property of the MDP
  Use a pseudo random walk to
  collect samples
  Once it is done, calculate the
  initial set of weights and Q values

## Slide 35: Implementation
Exploitation phase:
  Percentage of the number of episodes that system have spent in each state during a particular experimental run. Each run is characterized by a different value of the “epsilon” factor = (0.9, 0.7, 0.4, 0.1).

## Slide 36: Implementation
The “worst case” scenario:
  The optimal and the worst performing service combinations switch performances (not highly probable – for a demonstration purpose only)

## Slide 37: Open issues
To find an optimal value for the “epsilon” factor:
  forcing the optimal service combination vs. versatility to condition changes
Scalability of the algorithm:
  emphasize on an exploration phase
Stopping rules

## Slide 38: Implementation – an improved use case
16 experimental service combinations (e.g A, CD, ABD …)
Pre-estimated influences for each combination
16 actions available at every state
One basis function per incentive – Phi1, Phi2 (e.g. end-to-end delay, average number of re-transmissions)

## Slide 39: Implementation – an improved use case
Exploration phase:
Calculate the initial set of weights (ω1, w2)
Calculate the initial set of Q values for every state/action pair

## Slide 40: Implementation – an improved use case
Exploitation phase (epsilon greedy)
  Results after 100 learning episodes, no disturbances present:

## Slide 41: Implementation – an improved use case
Exploitation phase:
Reaction to a network condition disturbance (worst case scenario)

## Slide 42: Implementation and results
Exploitation phase:
  Introducing a simple efficiency-improving procedure
  Q value threshold:
Effects:
No significant difference in the number of episodes spent in the optimal state
Significant reduction in the number of episodes spent in the worst performing states